K2000 Mixer Maps For CUBASE 3.1

1)K2000.MIX
     This  map  has volume,panning,and bank/program controls for  all  16 
channels.Use Extended program changes.CH 10 and 16 are just like the rest.

2)K2000FX.MIX
     This  map  is for real time selection and control of  effects  in  a 
multi-timbral  setup.The  bank FXPROGS included in this package  must  be 
loaded to use this map.Set the bank to the bank you loaded into.When  you 
select an effect it calls the program which uses that effect (by Extended 
program change).To use this as I intended you should have EFFECTS set  to 
Program CH16.The controllers on the lower page can be used to  record  an 
effect  setup  for the song and effect param changes in real  time.It  is 
doubtful  you would play the keymap on ch16 as it would change each  time 
you  selected a new effect.The advantage in this method is that the  same 
three  controllers are active in each effect (I have  programmed  various 
routings  for them - just modify them to suit you).There is room for  ten 
effects  of your own which you would save as 0-9 and assign  to  programs 
48-57 in the effects bank (don't forget to save FXPROGS to disk).

                                     Glenn Reither
                                     Melbourne, Australia

[ Glenn is contactable via email at: greg@loose.apana.org.au ]